## Slide 1
Department of Electrical and
Electronic Engineering
Haochen Wang · FURP Research Project · 2025–2026
Decision-Aware Electricity Price Forecasting for Battery Trading
From Transformer ablations to a locked, no-ID four-market forecasting-to-control system
TL;DR
A universal Transformer achieved lower MAE in all 12 locked comparisons, yet tail errors still weakened battery revenue. A shallow expert router reached 63.53 USD/node-day, but its +1.73 gain over the strongest static hybrid remained statistically uncertain.
Five-stage research programme built on a Transformer ablation foundation
FOUNDATION
Transformer ablations
FFN
12 component + 32 layer removals
Inputs, frequency, horizon and multivariate context were screened first. Removing the FFN caused the largest loss, with SMAPE worsening by 33% to 486%.
›
STAGE 1
Three-task system
DA
RT@DA
Rolling RT
24 h LP + 4 h MPC
Separate DA, RT-at-DA and rolling RT models were connected to day-ahead LP, four-hour MPC and a continuous two-settlement ledger.
›
STAGE 2
Decision-aware training
frozen forecasting
backbone
value
head
locked report-only gate
Value-aware objectives reduced validation cost from 123.06 to 108.94. The selected +0.63% gain failed the frozen report-only gate.
›
STAGE 3
Multi-market transfer
CAISO
ERCOT
NYISO
PJM
shared no-ID Transformer
One model without market or node IDs covered CAISO, ERCOT, NYISO and PJM. Development used leave-one-market-out evidence and one locked 2025 test.
›
STAGE 4
Tail adaptation
1.29% extreme-spread amplitude
Negative-price adapters, peak scaling, probability gates, Beta/GPD and Chronos-2 heads rarely survived cross-market, multi-seed gates.
›
STAGE 5
Expert selection
DLinear
DA
Transformer
RT
depth-2 router
63.53 USD/node-day
DLinear DA positions and Transformer rolling corrections were combined. The router improved the point estimate, while its confidence interval crossed zero.
Background and system overview
Battery trading couples forecasts made at different information times. Day-ahead prices determine the initial 24-hour plan, while real-time prices drive corrections after the plan has been locked. A model can lower average error and still reduce revenue when rare spreads change the charge or discharge action.
Research question
Can one information-safe model transfer across markets, support three forecast issue times and improve the battery decisions produced from those forecasts?
Frozen experimental contract
INFORMATION
EVALUATION
BATTERY
What is available?
NYISO
05:00 ET
CAISO
10:00 PT
ERCOT
10:00 CPT
PJM
11:00 ET
168 h visible history + future calendar only
No future realised signals · no market or node ID
When can evidence move?
2020–22
TRAIN
2023
SELECT
2024
FREEZE
2020–24
REFIT
2025
ONE TEST
Market-balanced then node-balanced
Three seeds averaged before the locked test
What can the battery do?
1 MW
η 0.95
0.4 MWh
continuous SOC operating band
3.6 MWh
No simultaneous charge and discharge
3% deviation band · degradation κ = 5.7 USD/MWh
Actions fixed before actual DA and RT settlement
4
US markets
64
nodes
3
forecast tasks
1
locked 2025 test
Method and findings
Detailed Stage 3: no-ID forecasting-to-control architecture
Each task keeps its own weights, loss and checkpoint while sharing one architecture and the same information boundary.
DA price
RT price
Load
Wind + solar
Calendar
SHARED TRANSFORMER BLUEPRINT
Context-robust
normalisation
Per-stream
2-layer encoders
F0/F1 source
fusion
Target queries
RoPE
Task-specific
price head
DA Transformer
D−1 · F1 · MAE · 24 h
RT-at-DA Transformer
D−1 · F0 · pseudo-Huber · 24 h
Rolling RT Transformer
hourly · F1 · MAE · next 4 h
Day-ahead LP
locks the 24-hour plan
Rolling 4-hour RT MPC
executes the first action
Actions are fixed before actual prices settle: DA leg + RT deviation − 5.7 × throughput − 2|pRT| × excess deviation
Locked 2025 evidence
12 / 12
lower MAE in every locked task-to-baseline comparison
Model | DA | RT-at-DA | Rolling RT
Transformer | 10.46 | 15.14 | 9.69
TimesFM-3 | 20.51 | 21.42 | 10.24
Pooled XGB | 11.18 | 15.72 | 10.05
DLinear | 11.77 | 16.81 | 12.61
Four-market macro MAE in USD/MWh. Lower values are better.
ERCOT net revenue (USD/node-day)
In-depth analysis: why profit lagged accuracy
Extreme spreads were compressed by 98.71%
The universal Transformer reduced average error, but captured only 1.29% of the observed amplitude in the top 1% DA–RT spread hours. Positive-spike recall was 0, so the optimizer missed the most valuable charge and discharge opportunities.
Routes tested after the universal model
Route | Purpose | Gate
NEG-E / NEG-A | negative-price events | failed
Peak scaling | restore spike amplitude | failed
Probability gates | predict positive spikes | recall 0
Beta / GPD | conditional tail magnitude | failed
Chronos-2 heads | foundation tail adapter | failed
Candidates had to pass cross-market, multi-seed and frozen economic gates. Most improvements did not survive all three.
Model complementarity survived
DLinear
DA positions
Transformer
rolling RT
depth-2 router
63.53
USD/node-day · +1.73 vs static hybrid · 95% CI [−1.24, 4.75]
Claim boundary: the router confidence interval crosses zero. Cross-market economic superiority remains unproven until CAISO, NYISO and PJM settlement contracts receive equivalent validation.
TAKEAWAY Forecast accuracy transferred across markets, but economic value remained concentrated in rare price tails.
NEXT Validate local settlement rules and improve calibrated spike amplitude
Chart: 
| Transformer | Pooled XGB | DLinear | Static hybrid | Tail router
Revenue | 28.04 | 44.43 | 61.53 | 61.8 | 63.53
NORMALIZED EXTREME-SPREAD AMPLITUDE
Chart: 
| Observed top 1% | Transformer forecast
Amplitude retained | 100 | 1.29
Observed extreme spread = 100% · Transformer retained 1.29%
Lower average MAE did not preserve the price spikes that drive battery value.
Notes: Project evidence sources:
- docs/archive/参数消融汇报材料.md
- docs/archive/结构消融汇报材料.md
- docs/progress/25_偏差罚金合同审计与重训练.md
- docs/progress/38_四市场起报合同与缓存隔离修正.md
- docs/progress/46_多节点结果口径修订与无ID通用模型路线.md
- docs/progress/54_2025一次性锁定测试最终结论.md
- docs/progress/93_全阶段研究流程总览.md
- docs/progress/94_Chronos2尾部后训练探索统一结论.md
- data/results/tail_expert_router_v1/followup_2025_audit_v1.json
Design references:
- https://neurips.cc/virtual/2024/poster/95120
- https://neurips.cc/virtual/2024/106275
- https://cvpr.thecvf.com/virtual/2024/poster/30350
- https://cvpr.thecvf.com/virtual/2024/poster/29230
A1 typography guidance:
- https://www.ctl.ox.ac.uk/guidelines-for-submissions
- https://library.port.ac.uk/academic-support/presentations-and-group-work/academic-posters
- https://libguides.shu.ac.uk/researchposters/style
The router is a post-original-test fixed follow-up. No further 2025 tuning is allowed. Profit claims outside ERCOT remain limited by local settlement-contract validation.